RSA encryption implemented in VHDL
Using Montgomery multiplicaiton

---
Solution overview
Using Montgomery modular multipliciation
«Montgomery plane»
Two functions
MonPro
ModExp
Can be improved

---
Improvements
r mod n(r_n) and r^2 mod (rr_n) are supplied
  - Calculation of M is sped up
Parallellisation of MonPro
  - Doubles speed (in theory)
Stop loop after the most
significant 1-bit.
  - Speed increase when e < 128 bit
Pre-calculate whether n has to be added in MonPro
  - By performing: u[0]⊕A[i]B[0]. Speeds up MonPro.

---
MonPro diagram

---
ModExp diagram

---
Verification
Wrote a Python script
  - Using Montgomery multiplication
Started with the MonPro
Verified and tested that before continuing
Continued with ModExp
Verified and compared with Python

---
Results